## Slide 1: K means algorithm accelerator IP
Project by:
Liora Huf
Eddy Sraiber
Supervised by:
Shahar Gino
TODO: add symbols of VLSI lab , technion

## Slide 2: Content
Introduction to K means algorithm
Problem definition
Possible solutions
Introduction to APB protocol
Introduction to the paper
Design and Implementation –Top level
Design and Implementation – Main modules
Design and Implementation – FSM
Design and Implementation – Pipeline Diagrams
Design and Implementation – Performance
Zero Order Verification
Synthesis & Results
Layout
Summary and Conclusions

## Slide 3: K means algorithm Intro
Clustering is the classification of object in different groups, or more precisely, the partitioning of a data set into subsets(clusters), so the data in each subset(ideally) share some common – often according to some defined distance measure.
K means algorithm is a algorithm develop to determine all the clusters at once of a data set
The k means clustering algorithm is an algorithm to cluster n objects based on attributes into k partitions, where k<n.
K means clustering is a simple partition method for clustering analysis and widely use in machine learning.
Each clusters is represented by the center of the cluster and the algorithm converges to stables centroids of clusters.

## Slide 4: K means algorithm
Given the cluster number K, the K-means algorithm is carried out in four steps:
Initialization: randomly setting the initial centroids.
Classification: assign each object to the cluster with the nearest centroid measured with a specific distance metric.
Centroid update: Compute new centroids of the clusters given the current partition.
Convergence check : Compare the new centroids calculated on previous steps with initial centroids. If they are as close as a small threshold constant, end the algorithm. Else, return to Classification step with the new centroids.

## Slide 6: Problem definition
The k means algorithm although simple, could take significant amount of iterations to converge.
For large data sets, running the algorithm in software level (for example in Matlab) could result in large latency and consume a lot of resources from the processor.
Build a dedicated component in hardware level, in order to accelerate the running time of the algorithm.
Possible solution

## Slide 7: The chosen solution - K means accelerator
The project based on the following paper: “FPGA Implementation of K-means Algorithm for Bioinformatics Application: An Accelerated Approach to Clustering Microarray Data” by Hanaa M. Hussain, Khaled Benkrid, Huseyin Seker, Ahmet T. Erdogan.
The motivation of the paper is the acceleration of the K means algorithm in order to process Microarrays which is a technique used in genome experiments to measure the expression level of many thousands of genes simultaneously.

## Slide 8: Introduction to APB Protocol
The Advanced Peripheral Bus (APB) is part of the Advanced Microprocessor Bus Architecture (AMBA) protocol family. This protocol is a single master multi slave and set guidelines for transactions between the master and its low-bandwidth peripherals, the slaves. The APB protocol signal transactions are only related to the rising edge of the clock and every transaction takes at least two cycles. It can be used to provide access to the programmable control registers of peripheral devices. Furthermore, the APB is a low-cost interface that is optimal for minimal power consumption.

## Slide 9: APB Protocol -signals
Signal | Source | Description
PCLK | Clock source | Clock. The rising edge of PCLK times all transfers on the APB.
PRESETn | System bus equivalent | Reset. The APB reset signal is active LOW. This signal is normally connected directly to the system bus reset signal.
PADDR | Master | Address. This is the APB address bus. It can be up to 32 bits wide and is driven by the peripheral bus bridge unit.
PSELx | Master | Select. The APB bridge unit generates this signal to each peripheral bus slave. It indicates that the slave device is selected and that a data transfer is required. There is a PSELx signal for each slave.
PENABLE | Master | Enable. This signal indicates the second and subsequent cycles of an APB transfer.
PWRITE | Master | Direction. This signal indicates an APB write access when HIGH and an APB read access when LOW.
PWDATA | Master | Write data. This bus is driven by the peripheral bus bridge unit during write cycles when PWRITE is HIGH. This bus can be up to 32 bits wide.
PREADY | Slave | Ready. The slave uses this signal to extend an APB transfer.
PRDATA | Slave | Read Data. The selected slave drives this bus during read cycles when PWRITE is LOW. This bus can be up to 32-bits wide.
PSLVERR | Slave | This signal indicates a transfer failure. APB peripherals are not required to support the PSLVERR pin. This is true for both existing and new APB peripheral designs. Where a peripheral does not include this pin then the appropriate input to the APB bridge is tied LOW.

## Slide 10: APB Protocol – operating states
The state machine operates through the following states:
IDLE - This is the default state of the APB.
SETUP - When a transfer is required the bus moves into the SETUP state, where the appropriate select signal, PSELx, is asserted. The bus only remains in the SETUP state for one clock cycle and always moves to the ACCESS state on the next rising edge of the clock.
ACCESS - The enable signal, PENABLE, is asserted in the ACCESS state. The
address, write, select, and write data signals must remain stable during
the transition from the SETUP to ACCESS state. Exit from the ACCESS state is controlled by the PREADY signal from the slave:
• If PREADY is held LOW by the slave then the peripheral bus remains in the ACCESS state.
• If PREADY is driven HIGH by the slave then the ACCESS state is exited and the bus returns to the IDLE state if no more transfers are required. Alternatively, the bus moves directly to the SETUP state if another transfer follows.

## Slide 11: APB Protocol –Operating states
The figure bellow describes the operating states of the protocol:

## Slide 12: APB Transactions
Write Transfer
Read Transfer

## Slide 13: The paper
“FPGA Implementation of K-means Algorithm for Bioinformatics Application: An Accelerated Approach to Clustering Microarray Data” by Hanaa M. Hussain, Khaled Benkrid, Huseyin Seker, Ahmet T. Erdogan.
The motivation of the paper is the acceleration of the K means algorithm in order to process Microarrays which is a technique used in genome experiments to measure expression level of many thousands of genes simultaneously.

## Slide 14: Hardware implementation

## Slide 15: Design an Implementation – Top level
The high-level architecture proposed by this project is as shown. It is essentially composed of two main modules: the “Register file” and the “K means core”.
The “Register file” interfaces with the CPU host by APB protocol, as APB slave. Besides that, it also stores important data at local registers and interfaces with the second module “K means core”, allowing to read and write to its internal registers.
The “K means core” module is the actual “brain” of the architecture. It is responsible by running the algorithm and when it is done, it throws an interrupt to the CPU host, indicating the algorithm has come to an end.
The data set with which the algorithm is done is stored in a local RAM inside the “K means core module”. In order to do so, every data point is store one by one in this RAM by a process called “Indirect Access”.
The “Indirect Access” process is as its sounds: the CPU can write to the “K means core” local RAM only though a mediator, in this case, through the “Register File”.

## Slide 16: Design and Implementation – Main Modules
Register File
K means Core – Controller
K means Core – Classification Block
K means Core – New Means Calculation Block
K means Core – Convergence Check Block

## Slide 17: K means core
The proposed architecture for the k means core block is as described in the figure attached. This block is responsible for running the k means algorithm. It receives the input data points from the register file block by indirect access, as well as the initial centroids. The block output (to the register file block) is the final centroids value after the algorithm has ended and an interrupt indicating the calculation has been finished.

## Slide 18: K means core - controller state machine
The k means core controller is a state machine who controls the core setting signals connected to the other blocks in the core and to the register file block.

## Slide 19: K means core – Classification Block
The “Classification block” is a pipelined component which classifies the input data points into cluster by adding the data point to one of eight registers called “Accumulator X register” (X is an integer from 1 to 8). It has a throughput of one data point per cycle (after each cycle, one data point is added to the correct accumulator) but it has a latency of four cycles(one for reading the data from the RAM, one for calculating the distance between the centroid and the point, one to determine to closest centroid and one for adding to point to the accumulator.

## Slide 20: K means core - Classification block first part
The distance calculation from the input data point (stored in the “Input register”) to the centroids, which are stored in local registers called “Centroid Register X” (X being a integer from 1 to 8). This calculation is done by o module called “Distance calculator” which is basically two sub modules in series: the first calculates the subtraction of the data in the input register from the data in centroid register “X”, the second is a module which calculates the absolute value of the mentioned subtraction.

## Slide 21: K means core: Classification block second part
The second part is the minimum distance calculation. In this part, all the distances from the first are compared, and in the index of the closest centroid is found and given as output of this block

## Slide 22: K means core: Classification block third part
The third and final part of the Classification block pipeline is the accumulation of the input data point in the desired accumulator register, chosen by the index received from second part. In this part, there are sixteen registers: eight accumulators registers and eight counters registers. Each accumulator represents a cluster and stores the summed of all points assign to this cluster at a given time. The counters are register which simply keep track of how many points were assigned to each cluster. The index received from the previous part is used as a selector for two decoders, in order to choose to each accumulator, register and counter register the input data point should be added.

## Slide 23: K means core: new means calculation block - Division method
Duo to the complexity and time demanding characteristics of the floating point representation, the proposed architecture works with the fixed point representation. Therefore, there was a need to find a proper way to divide fixed point values.
The proposed method was to convert the fixed point number to an integer by shifting all fractional bits left (multiplying by 1024 ), dividing the converted number by using an integer divider(with known an simple algorithms, as describe in section Division in Hardware in the project report), and after the division shifting right the result in order to return to the fixed point representation.

## Slide 24: K means core: New means Calculation block
The “New Means Calculation block” is responsible for centroids update step of the algorithm. It does so by dividing the value of each accumulator(stored at the local “Accumulator reg” register in the “Classification block”) by the number of points assigned to them(stored at the local “Accumulator counter reg” register in the “Classification block”).

## Slide 25: K means core: Convergence check block
The convergence check block is responsible for the convergence check step of the algorithm. It does so by checking if any of the new centroids calculated in the “New Means Calculation block” value is close enough (within a pre-decided threshold stored at “Threshold register ” in the register file) to its old value(the value stored in the beginning of the iteration, stored in local registers of the classification block).

## Slide 26: Why this architecture?
K means core pipeline view is divided into two pipelines, the division can be seen in the figure attached. The reason for this division is the Read-After-Write dependency between the 2 pipes. This results by having one pipe working while the other wait for it's results. The left pipe result is all data points classified to clusters, which then can be used to calculate the new means for next iteration (or the last means if there will be a convergence). Then for the next iteration of classifying the data points, the new means value has to be ready, therefore the first pipe will "sleep" until second pipe will finish bringing the result of calculating new means

## Slide 27: First Pipeline

## Slide 28: First PIPELINE latency
The latency of the first pipeline is the number of cycles to fill the pipeline, plus the amount of data points(duo to the fact that after filled, it has a throughput of 1 data point processed per cycle) plus the number of cycles to empty the pipeline:

## Slide 29: First PIPELINE THROUGHPUT
The throughput of the first pipeline, after neglecting the fill & empty of the pipe as seen in the former slide, will be classifying one data point per cycle(there are 4 in the pipe at each situation and pipe width is 4 as well).
The bandwidth therefore can calculated as point_size_in_Bytes/clk_cycle.
Example:
  point_size_in_Bytes = 10 [Bytes].
  Clk cycle = 2[ns]
  Bandwidth =

## Slide 30: Second Pipeline

## Slide 31: Second PIPELINE latency
The latency of the second pipeline eight times the number of cycle to calculate the division for the new centroid(2), plus the number of cycles to check the convergence of a centroid(1), and at the one extra cycle at the end:

## Slide 32: Second PIPELINE throughput
The throughput of the second pipeline is addressed by the need of 2 cycles for each division operation and one cycle for convergency check, therefore every 3 clk cycles there will be finished a decision regarding a new centroid’s convergency.
The bandwidth therefore can calculated as centroid_size/(3*clk_cycle).Example:
  centroid_size (in_Bytes) = 10 [Bytes].
  Clk cycle = 2[ns]
  Bandwidth =

## Slide 33: Total PIPELINE latency
Finaly, one iteration of the algorithm latency results in:
The overall latency of the k means core will therefore be:

## Slide 34: Verification

## Slide 35: Zero order verification
The testbench made in order to verify the implementation of the design described herein was called top_tb.sv. Its structure is as shown below. It is basically composed by an instantiation of the K means TOP (which is the verified DUT), a clock generator and a stimulus generator and driver.

## Slide 36: Zero order verification – test bench
Two actual tests were implemented in the described testbench:
Description | Test Bench Type
“Sanity check” test: this test verifies with a simple example the functionality of the k means top module. | Sanity
“Do nothing” test: this test verifies the case that k means top module should not change the initial centroid values because they are the same as the data points, therefore being the expected final centroid values. | Do Nothing

## Slide 37: Zero order verification – “Sanity Check” Results
The figure bellow demonstrates the full simulation done by the “Sanity check” test. In this figure, the main parts of the IP functionality were marked:
First, the testbench configures the centroid’s registers with their initial value, as well as the registers which contain the RAM first and final addresses. This part was named “Configure registers” in the attached figure.
Then, the testbench writes the data point to the RAM via indirect access. This part was named “Indirect writing to RAM” in the attached figure.
Finally, in attached figure, in the part called “Algorithm calculation”, centroid registers, accumulators and accumulator counters can be seen changing with the progress of the algorithm. Also, in this part, the “Has converged” signal was marked in its rising edge, meaning the algorithm has reached convergence. Eight clock cycles after this occurs, the “interrupt” signal was marked in its rising edge, meaning the core is communicating to its host that it has finished its purpose.

## Slide 38: Zero order verification – “Do nothing test” Results
As it can be seen from the attached figure, the “Do nothing” test indeed works. It compares at its first iteration the initial centroid values with the calculated ones and concludes the algorithm has converged.

## Slide 39: Synthesis and Results
Technology:
    Synthesis Tool: design_vision Of Synopsys.
    Technology: TowerTSL018.
The synthesis took place with a symmetric clock, with frequency of 133.3 [MHz].
It is to be noted that the RAM's are working on negative clock.
There were no more constraints added to this synthesis process.
The slack is MET, as it can be seen form the attached report:

## Slide 40: Synthesis - Power and Area
From power report, the summary of total power can be obtained as follow:
From area report, the summary of areas can be obtained as follow:

## Slide 41: Layout
As extracted from Innovus tool, the chip utilization and chip area presented below:
Floorplan View

## Slide 42: Summary and conclusions
In this section, a brief summary of this project is done and our conclusions exposed. This section will be divided into three. First, a summary about the innovations in our design compared to the design present in the paper this project was based on. Then, an analysis of the achieved performance of the IP and finally a section describing future improvements of the IP.

## Slide 43: Summary and conclusions – Design Innovations
One main different are the units used for the architecture – the proposed paper has a specific RAM and DIV units. Due to academical limits – there was a choice for a DIV that will provide performance despite this limitation – for more refer to section ‎2.6.2.3.
Another difference is the interface description. Although the paper proposes an IP architecture, it does not explicit explain the interface specifications, therefore not being clear how the IP could be integrated with a CPU. In our design, there is a clear interface description as described in section ‎2.5. Because of its simplicity and wide use in the industry, we choose to use APB communication protocol (as presented in chapter 1 - where the CPU should be the master and the K means IP is the slave) as our interface protocol.
The last main difference we would like to mention is the micro architecture implementation extension. Even though the paper presents a k means-core architecture, it does not extend on the low level implementation. In our project, micro architecture, down to private implementation, was extended.

## Slide 44: Summary and conclusions – Achieved Performance
The total running time of the algorithm in our IP for the example described in section ‎4.2.1 was of 167*10^7 [fsec]=1.67 [μsec] for a simulation done with clock cycle set at 10 [nsec]. Duo to the fact that in our Synthesis process we set the clock cycle to be 7.5[nsec], the actual running time of the K means IP for the example described in section ‎4.2.1 was would be a total of 1.2525[μsec] .
In the other hand, the Matlab script used to verified the correctness of the output for input example described in section ‎4.2.1 took approximately 1.68 [sec], meaning the speedup for the algorithm using the IP was of 1.34*10^6.

## Slide 45: Summary and conclusions – Future improvements
• The use of large dividers affects not only the total area size, but also it sets the critical path. A way of solving (even if partially) this problem could be using smaller dividers, at the cost of the calculation accuracy. Future analysis could be done to the better describe the tradeoff between calculation accuracy and time and area constrains and choose the optimal DIVIDERS size.
• In our design, the number of clusters was predetermined to be eight. For future improvement, the code could be changed to allow the user to choose how many clusters to use in the algorithm.
• In our design, the input data size and dimensions were predetermined. For future improvement, the code could be changed to allow the user to choose the input data size and dimensions of the algorithm.
• A maximum iterations feature could be added to the design. As it is not certain the number of iterations it will take for the algorithm to reach convergence, a future register could be added enabling the user to set maximum number of iterations wanted to be ran, ending the algorithm after this predetermined number of iterations whether convergence has been achieved or not.
• Duo to the chosen architecture of two data dependent pipelines which run in series, the clock domain could be improved by having one clock for each pipeline. In this manner, at least one of the pipelines (the slower one between the two) could have better performance, improving the overall performance. This could possible be done also for the Register File, allowing the APB communications to be faster and therefore improving even more the total performance.

## Slide 46: Thank you